## Slide 1: Safe Control Synthesis via Input Constrained Control Control Barrier Functions

## Slide 2: Outline
Background and Problem Statement
Motivating Idea
Formal Construction
Simulation Results
Conclusions

## Slide 3: Background and Problem Statement
Safety Critical Controls
  What is it?
  Motivate it in terms of the ISS?
Overall objective:
  Given some nonlinear dynamical system xdot = f(x, u) => xdot = f(x) + g(x) u
  And a set of safe sets S = { x | h(x) geq 0}
  What control inputs can we apply such that the system never exits the safe set?

## Slide 4: The Control Barrier Function Approach
Simple and elegant solution:
Suppose for some h(t), we knew that hdot >= -\alpha h
Then we know that
h(t) \geq h(t_0) exp(-\alpha t) and h(t_0) > 0, then => h(t) \geq 0 for all t.
If we apply this to our control system:
Suppose hdot … then we know that the system never exits the safe set (a few additional assumptions are needed, but will be covered in our paper when we get there, for the CBFs refer to the cited paper)
Generalise to any class-K function (animate a few options)
Citation to Ames

## Slide 5: Challenges?
Look at the requirements for h:
We need it to satisfy the definition, which includes input constraints.
But what if that cant happen?
Toy Example with the 1D system
This paper introduces a method to convert a safety condition h(x) to a barrier function b(x) that respects the input constraints

## Slide 6: Formal Problem Statement
Given: (give dimensions, compactness etc)
  Dynamics xdot = f(x) + g(x) u
  Input Constraints U
  Safe Set S = { x : h(x) > 0}
Find:
  A new inner safe set C* = { x : b(x) geq 0} (has been called other things recently, control invariant set)
  A set of allowable control inputs K_{ICCBF}(x)
Such that
  If x(t_0) \in C* and u(x) \in K_{ICCBF}(x) => x(t) \in C* \forall t > 0
Ignores:
  State Estimation and Noise
Focus: cases where its known that h(x) is not a valid CBF.

## Slide 7: Outline Slide

## Slide 8: Motivating Idea
Draw the safe set
Draw that some point on this boundary will exit the safe set
Draw that we want to remove these states from the safe set
Suggest a formula:
b(x) = inf_{u \in U) (Lfh(x) + Lgh(x) u + \alpha h(x))
In words:
b(x) =the smallest (hdot + alpha h) over all u \in U

## Slide 9: Motivating Idea
This function b has a really useful property:
(demonstrate)
For the moment, assume C can be forward invariant. Then we are done.

## Slide 10
We have shifted the requirement from S to be forward invariant to requiring C to be forward invariant – but critically we have removed the states from S that certainly cannot be forward invariant.
Notice that the approximation can be made tighter or looser by changing alpha
But how do we know that C can be forward invariant under control inputs?
If it isn’t, we can simply repeat this step:
  Demonstrate in animation
  And maybe C2 will be forward invariant.

## Slide 11: Lets apply this to the 1D example:
Work through the 1D example

## Slide 12: Outline

## Slide 13: Formal Construction
Work through the construction steps
Define the ICCBF
Claim the theorem
Proof is in the paper, but follows from the same arguments made above

## Slide 14: Recap
We took any arbitrary h(x)
Recursively trimmed away the states we didn’t like until we got to one that we did like
How do we verify if a function is an ICCBF?
  Analytically - as we did in the 1d example
  Approximately analytically - demonstrate
  Still an open question of under which conditions do inner safe sets exist? Does this process converge?

## Slide 15: Three remarks
Quadratic Programs
Simple ICCBFs
Generalisation of Higher Order CBFs

## Slide 16: Outline

## Slide 17: Simulation Results
Adaptive Cruise Control

## Slide 18: Simulation Results
ISS chaser

## Slide 19: Conclusions
Key Contributions
Code is open sourced

## Slide 20: Fin.